## Slide 1: CS15-346 Perspectives in Computer Architecture
Single and Multiple Cycle Architectures
Lecture 5
January 28th, 2013

## Slide 2: Objectives
Origins of computing concepts, from Pascal to Turing and von Neumann.
Principles and concepts of computer architectures in 20th and 21st centuries.
Basic architectural techniques including instruction level parallelism, pipelining, cache memories and multicore architectures
Architecture including various kinds of computers from largest and fastest to tiny and digestible.
New architectural requirements far beyond raw performance such as energy, programmability, security, and availability.
Architectures for mobile computing including considerations affecting hardware, systems, and end-to-end applications.

## Slide 3: Where is “Computer Architecture”?
Architecture
“Computer Architecture is the science and art of selecting and interconnecting hardware components to create computers that meet functional, performance and cost goals.”
I/O system
Processor
Compiler
Operating
System
(Windows)
Application
Digital Design
Circuit Design
Instruction Set
Architecture
Datapath & Control
transistors
Memory
Hardware
Software
Assembler

## Slide 4: Design Constraints & Applications
Commercial
Scientific
Desktop
Mobile
Embedded
Smart sensors
Functional
Reliable
High Performance
Low Cost
Low Power

## Slide 5: Moore’s Law
2 * transistors/Chip Every 1.5 to 2.0 years

## Slide 6: Moore’s Law - Cont’d
Gordon Moore – cofounder of Intel
Increased density of components on chip
Number of transistors on a chip will double every year
Since 1970’s development has slowed a little
  Number of transistors doubles every 18 months
Cost of a chip has remained almost unchanged
Higher packing density means shorter electrical paths, giving higher performance
Smaller size gives increased flexibility
Reduced power and cooling requirements
Fewer interconnections increases reliability

## Slide 7: Single Cycle to Superscalar
Intel Pentium4 (2003)
Application: desktop/server
Technology: 90nm (1/100x)
55M transistors (20,000x)
101 mm2 (10x)
3.4 GHz (10,000x)
1.2 Volts (1/10x)
32/64-bit data (16x)
22-stage pipelined datapath
3 instructions per cycle (superscalar)
Two levels of on-chip cache
Data-parallel vector (SIMD) instructions, hyperthreading
Intel 4004 (1971)
Application: calculators
Technology: 10000 nm
2300 transistors
13 mm2
108 KHz
12 Volts
4-bit data
Single-cycle datapath

## Slide 8: Moore’s Law—Walls
A number of “walls”
  Physical process wall
    Impossible to continue shrinking transistor sizes
    Already leading to low yield, soft-errors, process variations
  Power wall
    Power consumption and density have also been increasing
  Other issues:
    What to do with the transistors?
    Wire delays

## Slide 9: Single to Multi Core
Intel Pentium4 (2003)
Application: desktop/server
Technology: 90nm (1/100x)
55M transistors (20,000x)
101 mm2 (10x)
3.4 GHz (10,000x)
1.2 Volts (1/10x)
32/64-bit data (16x)
22-stage pipelined datapath
3 instructions per cycle (superscalar)
Two levels of on-chip cache
Data-parallel vector (SIMD) instructions, hyperthreading
Intel Core i7 (2009)
Application: desktop/server
Technology: 45nm (1/2x)
774M transistors (12x)
296 mm2 (3x)
3.2 GHz to 3.6 Ghz (~1x)
0.7 to 1.4 Volts (~1x)
128-bit data (2x)
14-stage pipelined datapath (0.5x)
4 instructions per cycle (~1x)
Three levels of on-chip cache
data-parallel vector (SIMD) instructions, hyperthreading
Four-core multicore (4x)

## Slide 10: How much progress?
Item | Alto, 1972 | Chuck’s home PC, 2012 | Factor
Cost | $ 15,000 ($105K today) | $850 | 125
CPU clock rate | 6 MHz | 2.8 GHz (x4) | 1900
Memory size | 128 KB | 6 GB | 48000
Memory access | 850 ns | 50 ns | 17
Display pixels | 606 x 808 x 1 | 1920 x 1200 x 32 | 150
Network | 3 Mb Ethernet | 1 Gb Ethernet | 300
Disk capacity | 2.5 MB | 700 GB | 280000

## Slide 11: Anatomy: 5 Components of Computer
Computer
Processor
Computer
Control
(“brain”)
Datapath
(“work”)
Memory
(where
programs & data
reside when
running)
Devices
Input
Output
Keyboard, Mouse
Display, Printer
Disk (where
programs
& data
live when
not running)
Notes: That is, any computer, no matter how primitive or advance, can be divided into five parts:
1. The input devices bring the data from the outside world into the computer.
2. These data are kept in the computer’s memory until ...
3. The datapath request and process them.
4. The operation of the datapath is controlled by the computer’s controller.
All the work done by the computer will NOT do us any good unless we can get the data back to the outside world.
5. Getting the data back to the outside world is the job of the output devices.
The most COMMON way to connect these 5 components together is to use a network of busses.

## Slide 12: The Five Components of a Computer

## Slide 13: Multiplication – longhand algorithm
Just like you learned in school
For each digit, work out partial product (easy for binary!)
Take care with place value (column)
Add partial products

## Slide 14: Example of shift and add multiplication
 |  |  |  | 1 | 0 | 1 | 1
 |  |  | x | 1 | 1 | 0 | 1
 |  |  |  | 1 | 0 | 1 | 1
 |  |  | 0 | 0 | 0 | 0 | 
 |  |  | 0 | 1 | 0 | 1 | 1
 |  | 1 | 0 | 1 | 1 |  | 
 |  | 1 | 1 | 0 | 1 | 1 | 1
 | 1 | 0 | 1 | 1 |  |  | 
1 | 0 | 0 | 0 | 1 | 1 | 1 | 1
How many steps?
How do we implement this in hardware?

## Slide 15: Unsigned Binary Multiplication

## Slide 16: Execution of Example

## Slide 17: Flowchart for Unsigned Binary Multiplication

## Slide 18: Multiplying Negative Numbers
This does not work!
Solution 1
  Convert to positive if required
  Multiply as above
  If signs were different, negate answer
Solution 2
  Booth’s algorithm

## Slide 19: FP Addition & Subtraction Flowchart

## Slide 20: Floating point adder

## Slide 21: Execution of a Program

## Slide 22: Program -> Sequence of Instructions

## Slide 23: Function of Control Unit
For each operation a unique code is provided
  e.g. ADD, MOVE
A hardware segment accepts the code and issues the control signals
We have a computer!

## Slide 24: Computer Components: Top Level View
Data
Bus
Address
Bus
CPU
Memory
Control
Register
File
Functional
Units
IR
PC
Instructions
Data

## Slide 25: Instruction Cycle
Two steps:
  Fetch
  Execute

## Slide 26: Fetch Cycle
Program Counter (PC) holds address of next instruction to fetch
Processor fetches instruction from memory location pointed to by PC
Increment PC (PC = PC + 1)
  Unless told otherwise
Instruction loaded into Instruction Register (IR)
Processor interprets instruction

## Slide 27: Execute Cycle
Processor-memory
  Data transfer between CPU and main memory
Processor I/O
  Data transfer between CPU and I/O module
Data processing
  Some arithmetic or logical operation on data
Control
  Alteration of sequence of operations
  e.g. jump
Combination of above

## Slide 28: Instruction Set Architecture
SW/HW Interface
I/O system
Processor
Compiler
Operating
System
(Windows)
Application
Digital Design
Circuit Design
Instruction Set
Architecture
Datapath & Control
transistors
Memory
Hardware
Software
Assembler
ISA:
• A well-defined hardware/software interface
• The “contract” between software and hardware

## Slide 29: What is an instruction set?
The complete collection of instructions that are understood by a CPU
Machine Code
Binary
Usually represented by assembly codes
Notes: 2

## Slide 30: Elements of an Instruction
Operation code (Op code)
  Do this operation
Source Operand reference
  To this value
Result Operand reference
  Put the answer here
Notes: 3

## Slide 31: Operation Code
Operation code (Opcode)
  Do this operation
Name | Mnemonic
Addition | ADD
Subtraction | SUB
… | …
Multiply | MULT

## Slide 32: Instruction Design: Add R0, R4, R11
Add | R1, | R2, | R3
001 | 01 | 10 | 11
OpCode | Destination Register | Source Register | Source Register
3-bits | 2-bits | 2-bits | 2-bits
9-bits Instruction |  |  | 

## Slide 33: Add R1, R2, R3 ;(= 001011011)
Register File
Functional Units
I.R.
P.C.
001011011
0
1
2
3
4
5
6
7
2
2
001011011
001011011
...
3
CPU
Memory
What happens inside the CPU?

## Slide 34: Add R1, R2, R3 ;(= 001011011)
I.R.
P.C.
3
001011011
+
010101010
001010101
...
R1
R2
R3
010101010
001010101
011111111
Next Instruction
4
CPU

## Slide 35: Execution of a simple program
The following program was loaded in memory starting from memory location 0.
0000 Load R2, ML4 ; R2 = (ML4) = 5 = 1012
0001 Read R3, Input14 ; R3 = input device 14 = 7
0010 Sub R1, R3, R2 ; R1 = R3 – R2 = 7 – 5 = 2
0011 Store R1, ML5 ; store (R1) = 2 in ML5

## Slide 36: The Program in Memory
Load | R2, | ML4 | 
010 | 10 | 0100 | 
Read | R3, | Input14 | 
100 | 11 | 0100 | 
Sub | R1, | R3, | R2
000 | 01 | 11 | 10
Store | R1, | ML5 | 
011 | 01 | 0101 | 
0 | 0000 | 010100110
1 | 0001 | 100110100
2 | 0010 | 000011110
3 | 0011 | 011010111
4 | 0100 | 000000101
… | … | Don’t care
14 | 1011 | Input Port
15 | 1111 | Output Port
Address |  | Content

## Slide 37: Load R2, ML4 ; 010100110
I.R.
P.C.
010100110
Load
...
R1
R2
R3
000000101
0
CPU
1

## Slide 38: Read R3, Input14 ; 100110100
Read
...
R1
R2
R3
000000101
CPU
1
2
010100110
100110100
000000111

## Slide 39: Sub R1, R3, R2 ; 000011110
Sub
...
R1
R2
R3
000000101
CPU
2
3
100110101
000000111
000000101
000000010
000000111
000011110

## Slide 40: Store R1, ML5 ; 011010111
Don’t Care
...
R1
R2
R3
000000101
CPU
3
4
011010111
Next Instruction
000000010
000000111
Store

## Slide 41: In Memory
Before Program Execution
0 | 0000 | 010100110
1 | 0001 | 100110100
2 | 0010 | 000011110
3 | 0011 | 011010111
4 | 0100 | 000000101
5 | 0101 | Don’t care
… | … | Don’t care
14 | 1011 | Input Port
15 | 1111 | Output Port
Address |  | Content
000000010
After Program Execution

## Slide 42: Computer Performance
Response Time (latency) — How long does it take for my job to run? — How long does it take to execute a job? — How long must I wait for the database query?
Throughput — How many jobs can the machine run at once? — What is the average execution rate? — How much work is getting done?
Notes: Have them raise their hands when answering questions

## Slide 43: Execution Time
Elapsed Time (wall time)
  counts everything (disk and memory accesses, I/O , etc.)
  a useful number, but often not good for comparison purposes

## Slide 44: Execution Time
CPU time
  Does not count I/O or time spent running other programs
  Can be broken up into system time, and user time
  Our focus: user CPU time
  Time spent executing the lines of code that are "in" our program

## Slide 45: Definition of Performance
For some program running on machine X, PerformanceX = 1 / Execution timeX
"X is n times faster than Y" PerformanceX / PerformanceY = n

## Slide 46: Definition of Performance
Problem:
  machine A runs a program in 20 seconds
  machine B runs the same program in 25 seconds

## Slide 47
How to compare the performance?
Total Execution Time : A Consistent Summary Measure
Comparing and Summarizing Performance
 | Computer A | Computer B
Program1(sec) | 1 | 10
Program2(sec) | 1000 | 100
Total time (sec) | 1001 | 110

## Slide 48: Clock Cycles
Instead of reporting execution time in seconds, we often use cycles:
Clock “ticks” indicate when to start activities:
time

## Slide 49: Clock cycles
cycle time = time between ticks = seconds per cycle
clock rate (frequency) = cycles per second (1 Hz = 1 cycle/sec) A 4 Ghz clock has a 250ps cycle time

## Slide 50: CPU Execution Time
rate
clock
onds
cycle
onds
cycle
Cycle
Seconds
Cycles
Seconds
CPU
sec
/
sec
/
Program
cycles
Program
Program
time)
cycle
(clock
x
program)
a
for
cycles
clock
(CPU
program
a
for
time
execution
=
=
´
=
=

## Slide 51: How to Improve Performance
So, to improve performance (everything else being equal) you can either increase or decrease? ________ the # of required cycles for a program, or ________ the clock cycle time or, said another way, ________ the clock rate.

## Slide 52: How to Improve Performance
So, to improve performance (everything else being equal) you can either increase or decrease? _decrease_ the # of required cycles for a program, or _decrease_ the clock cycle time or, said another way, _increase_ the clock rate.

## Slide 53: How many cycles are required for a program?
Could we assume that # of cycles equals # of instructions
time
1st instruction
2nd instruction
3rd instruction
4th
5th
6th
...
This assumption is incorrect, different instructions take different amounts of time on different machines.

## Slide 54: Different numbers of cycles for different instructions
Multiplication takes more time than addition
Floating point operations take longer than integer ones
Accessing memory takes more time than accessing registers
Important point: changing the cycle time often changes the number of cycles required for various instructions
time

## Slide 55: Now that we understand cycles
Components of Performance | Units of Measure
CPU execution time for a program | Seconds for the program
Instruction count | Instructions executed for the program
Clock Cycles per Instruction (CPI) | Average number of clock cycles per instruction
Clock cycle time | Seconds per clock cycle
CPU time = Instruction count x CPI x clock cycle time

## Slide 56: Implementation vs. Performance
Performance of a processor is determined by
  Instruction count of a program
    The compiler & the ISA determine the instruction count.
  CPI
    The ISA & implementation of the processor determines the CPI.
  Clock cycle time (clock rate)
    The implementation of the processor determines the clock cycle time.
CPU time = Instruction count x CPI x clock cycle time

## Slide 57: CPI, Clocks Per Instruction
CPU clock cycles = Instructions for a program
x Average clock cycles per Instruction (CPI)
CPU time = Instruction count x CPI x clock cycle time

## Slide 58: Performance
Performance is determined by execution time
Do any of the other variables equal performance?
  # of cycles to execute program?
  # of instructions in program?
  # of cycles per second?
  average # of cycles per instruction?
  average # of instructions per second?
Common pitfall: thinking one of the variables is indicative of performance when it really isn’t.

## Slide 59: CPU Clock Cycles
CPIi : the average number of cycles per instructions for that instruction class
Ci : the count of the number of instructions of class i executed.
n : the number of instruction classes.

## Slide 60: Example
Instruction Classes:
  Add
  Multiply
Average Clock Cycles per Instruction:
  Add 1cc
  Mul 3cc
Program A executed:
  10 Add instructions
  5 Multiply instructions

## Slide 61: CISC vs. RISC
CISC (Complex Instruction Set Computing) ISAs
  Complex instructions
  Low instructions in a program
  Higher CPI and cycle time
RISC (Reduced Instruction Set Computer)
  Simple instructions
  Low CPI and cycle time
  Higher instructions in a program

## Slide 62: The Big Picture of a Computer System
Datapath
Control
Processor
Main Memory
Input / Output

## Slide 63: Focusing on CPU & Memory
Register File
ALU
Datapath
IR
PC
CPU
Memory
Data
Address
Control Unit

## Slide 64: The Datapath
A load / store machine (RISC), register – register where access to memory is only done by load & store operations.
Source 1
Register File
ALU
Source 2
Destination
Result
Control
: (Register File)

## Slide 65: The Datapath
A load / store machine (RISC), register – register where access to memory is only done by load & store operations.
Source 1
Register File
ALU
Source 2
Destination
Result
Control
: (ALU)

## Slide 66: Simple ALU Design
control
s1_bus
dest_bus
Add/Sub
s2_bus
Shift/Logic
16 to 8 MUX

## Slide 67: How about the Control?
Register File
ALU
Datapath
IR
PC
CPU
Memory
Data
Address
Control Unit

## Slide 68: The Control Unit
Control Logic

## Slide 69: FSM for addition in Load/Store Architecture
Fetch
Decode
Store result
ALU Execute
Store result in R1
Send signal to ALU to perform addition
Fetch Instruction (Add R1, R2)
Registers R1 and R2
Fetch next instruction

## Slide 70: The Control Unit When Add is Executing
Control Logic
Instruction
The control
Turns on
the required
lines. In the
Case of add,
Ex: ALU OP,
ALU source,
Etc.

## Slide 71: Possible Execution Steps of Any Instruction
Instruction Fetch
Instruction Decode and Register Fetch
Execution of the Memory Reference Instruction
Execution of Arithmetic-Logical operations
Branch Instruction
Jump Instruction

## Slide 72: Instruction Processing
Five steps:
  Instruction fetch (IF)
  Instruction decode and operand fetch (ID)
  ALU/execute (EX)
  Memory (not required) (MEM)
  Write-back (WB)
IF
ID
EX
MEM
WB

## Slide 73: Datapath & Control
Control

## Slide 74: Datapath Elements
The data path contains 2 types of logic elements:
  Combinational: (e.g. ALU) Elements that operate on data values. Their outputs depend on their inputs.
  State: (e.g. Registers & Memory) Elements with internal storage. Their state is defined by the values they contain.

## Slide 75: Pentium Processor Die
REG

## Slide 76: Abstract View of the Datapath

## Slide 77: Single Cycle Implementation
This simple processor can compute ALU instructions, access memory or compute the next instruction's address in a single cycle.
Clk
Single Cycle Implementation:
Load
ADD
Cycle 1
Cycle 2

## Slide 78: Possible Execution Steps of Any Instructions
Instruction Fetch
Instruction Decode and Register Fetch
Execution of the Memory Reference Instruction
Execution of Arithmetic-Logical operations
Branch Instruction
Jump Instruction

## Slide 79: Instruction Processing
Five steps:
  Instruction fetch (IF)
  Instruction decode and operand fetch (ID)
  ALU/execute (EX)
  Memory (not required) (MEM)
  Write-back (WB)
IF
ID
EX
MEM
WB

## Slide 80: Single Cycle Implementation

## Slide 81: Multiple ALUs and Memory Units

## Slide 82: Single Cycle Datapath

## Slide 83: What’s Wrong with Single Cycle?
All instructions run at the speed of the slowest instruction.
Adding a long instruction can hurt performance
  What if you wanted to include multiply?
You cannot reuse any parts of the processor
  We have 3 different adders to calculate PC+4, PC+4+offset and the ALU
No profit in making the common case fast
  Since every instruction runs at the slowest instruction speed
    This is particularly important for loads as we will see later

## Slide 84: What’s Wrong with Single Cycle?
  1 ns – Register read/write time
  2 ns – ALU/adder
  2 ns – memory access
  0 ns – MUX, PC access, sign extend, ROM
  add: 2ns + 1ns + 2ns + 1ns = 6 ns
  beq: 2ns + 1ns + 2ns = 5 ns
  sw: 2ns + 1ns + 2ns + 2ns = 7 ns
  lw: 2ns + 1ns + 2ns + 2ns + 1ns = 8 ns
Get read ALU mem write
Instr reg operation reg

## Slide 85: Computing Execution Time
Assume: 100 instructions executed
  25% of instructions are loads,
  10% of instructions are stores,
  45% of instructions are adds, and
  20% of instructions are branches.
Single-cycle execution:
100 * 8ns = 800 ns
Optimal execution:
25*8ns + 10*7ns + 45*6ns + 20*5ns = 640 ns

## Slide 86: Single Cycle Problems
A sequence of instructions:
    LW (IF, ID, EX, MEM, WB)
    SW (IF, ID, EX, MEM)
    etc
Clk
Single Cycle Implementation:
Load
Store
Waste
Cycle 1
Cycle 2
  what if we had a more complicated instruction like floating point?
  wasteful of area

## Slide 87: Multiple Cycle Solution
  use a “smaller” cycle time
  have different instructions take different numbers of cycles
  a “multicycle” datapath:

## Slide 88: Multicycle Approach
We will be reusing functional units
  ALU used to compute address and to increment PC
  Memory used for instruction and data
We will use a finite state machine for control

## Slide 89: The Five Stages of an Instruction
IF: Instruction Fetch and Update PC
ID: Instruction Decode and Registers Fetch
Ex: Execute R-type; calculate memory address
Mem: Read/write the data from/to the Data Memory
WB: Write the result data into the register file
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
IF
ID
Ex
Mem
WB
Notes: As shown here, each of these five steps will take one clock cycle to complete.

## Slide 90: Multicycle Implementation
Break up the instructions into steps, each step takes a cycle
  balance the amount of work to be done
  restrict each cycle to use only one major functional unit
At the end of a cycle
  store values for use in later cycles (easiest thing to do)
  introduce additional “internal” registers

## Slide 91: The Five Stages of Load Instruction
IF: Instruction Fetch and Update PC
ID: Instruction Decode and Registers Fetch
Ex: Execute R-type; calculate memory address
Mem: Read/write the data from/to the Data Memory
WB: Write the result data into the register file
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
IF
ID
Ex
Mem
WB
lw
Notes: As shown here, each of these five steps will take one clock cycle to complete.

## Slide 92: Multiple Cycle Implementation
Break the instruction execution into Clock Cycles
  Different instructions require a different number of clock cycles
  Clock cycle is limited by the slowest stage
  Instruction latency is not reduced (time from the start of an instruction to its completion)
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
IFetch
Dec
Exec
Mem
WB
lw
Cycle 7
Cycle 6
Cycle 8
sw
IFetch
Dec
Exec
Mem
WB
Cycle 9
Notes: Latency = execution time (delay or response time) – the total time from start to finish of ONE instruction
For processors one important measure is THROUGHPUT (or the execution bandwidth) – the total amount of work done in a given amount of time
For memories one important measure is BANDWIDTH – the amount of information communicated across an interconnect (e.g., bus) per unit time; the number of operations performed per second (the WIDTH of the operation and the RATE of the operation)

## Slide 93: Single Cycle vs. Multiple Cycle
Clk
Cycle 1
Multiple Cycle Implementation:
IFetch
Dec
Exec
Mem
WB
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
IFetch
Dec
Exec
Mem
lw
sw
Clk
Single Cycle Implementation:
Load
Store
Waste
IFetch
R-type
Cycle 1
Cycle 2
Notes: Here are the timing diagrams showing the differences between the single cycle, multiple cycle, and pipeline implementations.
For example, in the pipeline implementation, we can finish executing the Load, Store, and R-type instruction sequence in seven cycles.

## Slide 94: Multicycle Implementation
Break up the instructions into steps, each step takes a cycle
  balance the amount of work to be done
  restrict each cycle to use only one major functional unit
At the end of a cycle
  store values for use in later cycles (easiest thing to do)
  introduce additional “internal” registers

## Slide 95: Single Cycle vs. Multi Cycle
Single-cycle datapath:
Fetch, decode, execute one complete instruction every cycle
Takes 1 cycle to execution any instruction by definition (CPI=1)
Long cycle time to accommodate slowest instruction
(worst-case delay through circuit, must wait this long every time)
Multi-cycle datapath:
Fetch, decode, execute one complete instruction over multiple cycles
Allows instructions to take different number of cycles
Short cycle time
Higher CPI

## Slide 96: Pipelining and ILP
How can we increase the IPC? (IPC=1/CPI)
  CPU time = Instruction count x CPI x clock cycle time
Clk
Cycle 1
IFetch
Dec
Exec
Mem
WB
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
IFetch
Dec
Exec
Mem
lw
sw
IFetch
R-type