## Slide 1: CS15-346 Perspectives in Computer Architecture
Pipelining and Instruction Level Parallelism
Lecture 6
January 30th, 2013

## Slide 2: Objectives
Origins of computing concepts, from Pascal to Turing and von Neumann.
Principles and concepts of computer architectures in 20th and 21st centuries.
Basic architectural techniques including instruction level parallelism, pipelining, cache memories and multicore architectures
Architecture including various kinds of computers from largest and fastest to tiny and digestible.
New architectural requirements far beyond raw performance such as energy, programmability, security, and availability.
Architectures for mobile computing including considerations affecting hardware, systems, and end-to-end applications.

## Slide 3: Computer Performance
Response Time (latency) — How long does it take for my job to run? — How long does it take to execute a job? — How long must I wait for the database query?
Throughput — How many jobs can the machine run at once? — What is the average execution rate? — How much work is getting done?
Notes: Have them raise their hands when answering questions

## Slide 4: Computer Performance
CPU time = Seconds = Instructions x Cycles x Seconds
Program Program Instruction Cycle
inst count
CPI
Cycle time

## Slide 5: Performance
Components of Performance | Units of Measure
CPU execution time for a program | Seconds for the program
Instruction count | Instructions executed for the program
Clock Cycles per Instruction (CPI) | Average number of clock cycles per instruction
Clock cycle time | Seconds per clock cycle
CPU time = Instruction count x CPI x clock cycle time

## Slide 6: Single Cycle vs. Multiple Cycle
Clk
Cycle 1
Multiple Cycle Implementation:
IFetch
Dec
Exec
Mem
WB
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
IFetch
Dec
Exec
Mem
lw
sw
Clk
Single Cycle Implementation:
Load
Store
Waste
IFetch
R-type
Cycle 1
Cycle 2
Notes: Here are the timing diagrams showing the differences between the single cycle, multiple cycle, and pipeline implementations.
For example, in the pipeline implementation, we can finish executing the Load, Store, and R-type instruction sequence in seven cycles.

## Slide 7: Single Cycle vs. Multi Cycle
Single-cycle datapath:
Fetch, decode, execute one complete instruction every cycle
Takes 1 cycle to execution any instruction by definition (CPI=1)
Long cycle time to accommodate slowest instruction
(worst-case delay through circuit, must wait this long every time)
Multi-cycle datapath:
Fetch, decode, execute one complete instruction over multiple cycles
Allows instructions to take different number of cycles
Short cycle time
Higher CPI

## Slide 8: Pipelining and ILP
How can we increase the IPC? (IPC=1/CPI)
  CPU time = Instruction count x CPI x clock cycle time
Clk
Cycle 1
IFetch
Dec
Exec
Mem
WB
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
IFetch
Dec
Exec
Mem
lw
sw
IFetch
R-type

## Slide 9: Sequential Laundry
A
B
C
D
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time
30
30
30
30
30
30
30
30
30
30
30
30
washing = drying = folding = 30 minutes
1 load = 1.5 hours; 4 loads = 6 hours

## Slide 10: Sequential Laundry
A
B
C
D
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time
30
30
30
30
30
30
30
30
30
30
30
30
1 load = 1.5 hours; 4 loads = 3 hours

## Slide 11: Sequential Laundry
30
30
A
B
C
D
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time
30
30
30
30
A
B
C
D
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time
30
30
30
30
30
30
30
30
30
30
30
30
Ideal Pipelining:
3-loads in parallel
No additional resources
Throughput increased by 3
Latency per load is the same

## Slide 12: Sequential Laundry – a real example
A
B
C
D
30
40
20
30
40
20
30
40
20
30
40
20
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time
washing = 30; drying = 40; folding = 20 minutes
1 load = 1.5 hours; 4 loads = 6 hours

## Slide 13: Pipelined Laundry - Start work ASAP
Pipelined laundry takes 3.5 hours for 4 loads
Drying, the slowest stage, dominates!
A
B
C
D
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20

## Slide 14: Pipelining Lessons
Pipelining does not help latency of single task, it helps throughput of entire workload
Pipeline rate limited by slowest pipeline stage
Multiple tasks operating simultaneously
Potential speedup = Number pipe stages
Unbalanced lengths of pipe stages reduces speedup
Time to “fill” pipeline and time to “drain” it reduces speedup
A
B
C
D
6 PM
7
8
9
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20

## Slide 15: Pipelining
Does not improve latency!
Programs execute billions of instructions, so throughput is what matters!

## Slide 16: The Five Stages of Load Instruction
IFetch: Instruction Fetch and Update PC
Dec: Registers Fetch and Instruction Decode
Exec: Execute R-type; calculate memory address
Mem: Read/write the data from/to the Data Memory
WB: Write the result data into the register file
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
IFetch
Dec
Exec
Mem
WB
lw
Notes: As shown here, each of these five steps will take one clock cycle to complete.

## Slide 17: Pipelined Processor
Start the next instruction while still working on the current one
  improves throughput or bandwidth - total amount of work done in a given time (average instructions per second or per clock)
  instruction latency is not reduced (time from the start of an instruction to its completion)
  pipeline clock cycle (pipeline stage time) is limited by the slowest stage
  for some instructions, some stages are wasted cycles
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
IFetch
Dec
Exec
Mem
WB
lw
Cycle 7
Cycle 6
Cycle 8
sw
IFetch
Dec
Exec
Mem
WB
R-type
IFetch
Dec
Exec
Mem
WB
Notes: Latency = execution time (delay or response time) – the total time from start to finish of ONE instruction
For processors one important measure is THROUGHPUT (or the execution bandwidth) – the total amount of work done in a given amount of time
For memories one important measure is BANDWIDTH – the amount of information communicated across an interconnect (e.g., bus) per unit time; the number of operations performed per second (the WIDTH of the operation and the RATE of the operation)

## Slide 18: Single Cycle, Multiple Cycle, vs. Pipeline
Clk
Cycle 1
Multiple Cycle Implementation:
IFetch
Dec
Exec
Mem
WB
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
lw
IFetch
Dec
Exec
Mem
WB
IFetch
Dec
Exec
Mem
lw
sw
Pipeline Implementation:
IFetch
Dec
Exec
Mem
WB
sw
Clk
Single Cycle Implementation:
Load
Store
Waste
IFetch
R-type
IFetch
Dec
Exec
Mem
WB
R-type
Cycle 1
Cycle 2
“wasted” cycles
Notes: Here are the timing diagrams showing the differences between the single cycle, multiple cycle, and pipeline implementations.
For example, in the pipeline implementation, we can finish executing the Load, Store, and R-type instruction sequence in seven cycles.

## Slide 19: Multiple Cycle v. Pipeline, Bandwidth v. Latency
Clk
Cycle 1
Multiple Cycle Implementation:
IFetch
Dec
Exec
Mem
WB
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
lw
IFetch
Dec
Exec
Mem
WB
IFetch
Dec
Exec
Mem
lw
sw
Pipeline Implementation:
IFetch
Dec
Exec
Mem
WB
sw
IFetch
R-type
IFetch
Dec
Exec
Mem
WB
R-type
Latency per lw = 5 clock cycles for both
Bandwidth of lw is 1 per clock clock (IPC) for pipeline vs. 1/5 IPC for multicycle
Pipelining improves instruction bandwidth, not instruction latency
Notes: Here are the timing diagrams showing the differences between the single cycle, multiple cycle, and pipeline implementations.
For example, in the pipeline implementation, we can finish executing the Load, Store, and R-type instruction sequence in seven cycles.

## Slide 20: Ideal Pipelining
When the pipeline is full, after every stage one task is completed.
combinational logic (IF,ID,EX,M,WB)
T psec
BW=~(1/T)
BW=~(2/T)
T/2 ps (IF,ID,EX)
T/2 ps (M,WB)
BW=~(3/T)
T/3
ps (IF,ID)
T/3
ps (EX,M)
T/3
ps (M,WB)

## Slide 21: Pipeline Datapath Modifications
Read
Address
Instruction
Memory
Add
PC
4
0
1
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
1
0
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
1
0
What do we need to add/modify in our MIPS datapath?
  registers between pipeline stages to isolate them
IFetch/Dec
Dec/Exec
Exec/Mem
Mem/WB
IF:IFetch
ID:Dec
EX:Execute
MEM:
MemAccess
WB:
WriteBack
System Clock
Sign
Extend
Notes: Note two exceptions to right-to-left flow
WB that writes the result back into the register file in the middle of the datapath
Selection of the next value of the PC, one input comes from the calculated branch address from the MEM stage
Only later instructions in the pipeline can be influenced by these two REVERSE data movements.
The first one (WB to ID) leads to data hazards.
The second one (MEM to IF) leads to control hazards.
All instructions must update some state in the processor – the register file, the memory, or the PC – so separate pipeline registers are redundant to the state that is updated (not needed).
PC can be thought of as a pipeline register: the one that feeds the IF stage of the pipeline. Unlike all of the other pipeline registers, the PC is part of the visible architecture state – its content must be saved when an exception occurs (the contents of the other pipe registers are discarded).

## Slide 22: Graphically Representing the Pipeline
Can help with answering questions like:
  how many cycles does it take to execute this code?
  what is the ALU doing during cycle 4?
ALU
IM
Reg
DM
Reg

## Slide 23: Why Pipeline? For Throughput!
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Inst 0
Inst 1
Inst 2
Inst 4
Inst 3
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Once the pipeline is full, one instruction is completed every cycle
Time to fill the pipeline

## Slide 24: Important Observation
Each functional unit can only be used once per instruction (since 4 other instructions executing)
If each functional unit used at different stages then leads to hazards:
  Load uses Register File’s Write Port during its 5th stage
  R-type uses Register File’s Write Port during its 4th stage
2 ways to solve this pipeline hazard.
Ifetch
Reg/Dec
Exec
Mem
Wr
Load
1
2
3
4
5
Ifetch
Reg/Dec
Exec
Wr
R-type
1
2
3
4
Notes: I already told you that in order for pipeline to work perfectly, each functional unit can ONLY be used once per instruction.
What I have not told you is that this (1st bullet) is a necessary but NOT sufficient condition for pipeline to work.
The other condition to prevent pipeline hiccup is that each functional unit must be used at the same stage for all instructions.
For example here, the load instruction uses the Register File’s Wr port during its 5th stage but the R-type instruction right now will use the Register File’s port during its 4th stage.
This (5 versus 4) is what caused our problem. How do we solve it? We have 2 solutions.
+1 = 17 min. (X:57)

## Slide 25: Solution 1: Insert “Bubble” into the Pipeline
Insert a “bubble” into the pipeline to prevent 2 writes at the same cycle
  The control logic can be complex.
  Lose instruction fetch and issue opportunity.
No instruction is started in Cycle 6!
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Exec
Wr
R-type
Ifetch
Reg/Dec
Exec
Ifetch
Reg/Dec
Exec
Mem
Wr
Load
Ifetch
Reg/Dec
Exec
Wr
R-type
Ifetch
Reg/Dec
Exec
Wr
R-type
Pipeline
Bubble
Ifetch
Reg/Dec
Exec
Wr
Notes: The first solution is to insert a “bubble” into the pipeline AFTER the load instruction to push back every instruction after the load that are already in the pipeline by one cycle.
At the same time, the bubble will delay the Instruction Fetch of the instruction that is about to enter the pipeline by one cycle.
Needless to say, the control logic to accomplish this can be complex.
Furthermore, this solution also has a negative impact on performance.
Notice that due to the “extra” stage (Mem) Load instruction has, we will not have one instruction finishes every cycle (points to Cycle 5).
Consequently, a mix of load and R-type instruction will NOT have an average CPI of 1 because in effect, the Load instruction has an effective CPI of 2.
So this is not that hot an idea Let’s try something else.
+2 = 19 min. (X:59)

## Slide 26: Solution 2: Delay R-type’s Write by One Cycle
Delay R-type’s register write by one cycle:
  Now R-type instructions also use Reg File’s write port at Stage 5
  Mem stage is a NOP stage for R-type: nothing is being done.
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Exec
Mem
Wr
Load
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Exec
Wr
R-type
Mem
Exec
Exec
Exec
Exec
1
2
3
4
5
Notes: Well one thing we can do is to add a “Nop” stage to the R-type instruction pipeline to delay its register file write by one cycle.
Now the R-type instruction ALSO uses the register file’s witer port at its 5th stage so we eliminate the write conflict with the load instruction.
This is a much simpler solution as far as the control logic is concerned. As far as performance is concerned, we also gets back to having one instruction completes per cycle.
This is kind of like promoting socialism: by making each individual R-type instruction takes 5 cycles instead of 4 cycles to finish, our overall performance is actually better off.
The reason for this higher performance is that we end up having a more efficient pipeline.
+1 = 20 min. (Y:00)

## Slide 27: Can Pipelining Get Us Into Trouble?
Yes: Pipeline Hazards
  structural hazards: attempt to use the same resource by two different instructions at the same time
  data hazards: attempt to use data before it is ready
    instruction source operands are produced by a prior instruction still in the pipeline
    load instruction followed immediately by an ALU instruction that uses the load operand as a source value
  control hazards: attempt to make a decision before condition has been evaluated
    branch instructions
Can always resolve hazards by waiting
  pipeline control must detect the hazard
  take action (or delay action) to resolve hazards

## Slide 28: Structural Hazard
Attempt to use same hardware for two different things at the same time.
Solution 1: Wait
  Must detect hazard
  Must have mechanism to stall
Solution 2: Throw more hardware at the problem

## Slide 29: A Single Memory Would Be a Structural Hazard
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
lw
Inst 1
Inst 2
Inst 4
Inst 3
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
Reading data from memory
Reading instruction from memory

## Slide 30: How About Register File Access?
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
add r1,
Inst 1
Inst 2
Inst 4
add r2,r1,
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Potential read before write data hazard
Notes: For class handout

## Slide 31: How About Register File Access?
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Inst 1
Inst 2
Inst 4
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Can fix register file access hazard by doing reads in the second half of the cycle and writes in the first half.
add r1,
add r2,r1,
Potential read before write data hazard
Notes: For lecture
Define register reads to occur in the second half of the cycle and register writes in the first half

## Slide 32: Three Generic Data Hazards
Read After Write (RAW) InstrJ tries to read operand before InstrI writes it
Caused by a “Data Dependence” (in compiler nomenclature). This hazard results from an actual need for communication.
I: add r1,r2,r3
J: sub r4,r1,r3

## Slide 33: Three Generic Data Hazards
Write After Read (WAR) InstrJ writes operand before InstrI reads it
Called an “anti-dependence” by compiler writers. This results from reuse of the name “r1”.
I: sub r4,r1,r3
J: add r1,r2,r3
K: mul r6,r1,r7

## Slide 34: Three Generic Data Hazards
Write After Write (WAW) InstrJ writes operand before InstrI writes it.
Called an “output dependence” by compiler writers This also results from the reuse of name “r1”.
I: sub r1,r4,r3
J: add r1,r2,r3
K: mul r6,r1,r7

## Slide 35: Register Usage Can Cause Data Hazards
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r5
and r6,r1,r7
xor r4,r1,r5
or r8, r1, r9
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Dependencies backward in time cause hazards
Which are read before write data hazards?
Notes: For class handout

## Slide 36: Register Usage Can Cause Data Hazards
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r5
and r6,r1,r7
xor r4,r1,r5
or r8, r1, r9
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Dependencies backward in time cause hazards
Read before write data hazards
Notes: For lecture

## Slide 37: Loads Can Cause Data Hazards
I
n
s
t
r.
O
r
d
e
r
lw r1,100(r2)
sub r4,r1,r5
and r6,r1,r7
xor r4,r1,r5
or r8, r1, r9
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Dependencies backward in time cause hazards
Load-use data hazard
Notes: Note that lw is just another example of register usage (beyond ALU ops)

## Slide 38: One Way to “Fix” a Data Hazard
stall
stall
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
ALU
IM
Reg
DM
Reg
sub r4,r1,r5
and r6,r1,r7
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Can fix data hazard by waiting – stall – but affects throughput

## Slide 39: Another Way to “Fix” a Data Hazard
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
ALU
IM
Reg
DM
Reg
sub r4,r1,r5
and r6,r1,r7
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Can fix data hazard by forwarding results as soon as they are available to where they are needed.
xor r4,r1,r5
or r8, r1, r9
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Notes: For class handout

## Slide 40: Another Way to “Fix” a Data Hazard
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
ALU
IM
Reg
DM
Reg
sub r4,r1,r5
and r6,r1,r7
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Can fix data hazard by forwarding results as soon as they are available to where they are needed.
xor r4,r1,r5
or r8, r1, r9
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Notes: For lecture
Forwarding paths are valid only if the destination stage is later in time than the source stage.
Forwarding is harder if there are multiple results to forward per instruction or if they need to write a result early in the pipeline

## Slide 41: Forwarding with Load-use Data Hazards
I
n
s
t
r.
O
r
d
e
r
lw r1,100(r2)
sub r4,r1,r5
and r6,r1,r7
xor r4,r1,r5
or r8, r1, r9
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Will still need one stall cycle even with forwarding
Notes: Note that lw is just another example of register usage (beyond ALU ops)
Need to stall even with forwarding when data hazard involves a load

## Slide 42: Control Hazards
Caused by delay between the fetching of instructions and decisions about changes in control flow
  Branches
  Jumps

## Slide 43: Branch Instructions Cause Control Hazards
I
n
s
t
r.
O
r
d
e
r
lw
Inst 4
Inst 3
beq
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Dependencies backward in time cause hazards

## Slide 44: One Way to “Fix” a Control Hazard
stall
stall
stall
I
n
s
t
r.
O
r
d
e
r
beq
ALU
IM
Reg
DM
Reg
lw
ALU
IM
Reg
DM
Reg
ALU
Inst 3
IM
Reg
DM
Can fix branch hazard by waiting – stall – but affects throughput
Notes: Another “solution” is to put in enough extra hardware so that we can test registers, calculate the branch address, and update the PC during the second stage of the pipeline. That would reduce the number of stalls to only one.
A third approach is to prediction to handle branches, e.g., always predict that branches will be untaken. When right, the pipeline proceeds at full speed. When wrong, have to stall (and make sure nothing completes – changes machine state – that shouldn’t have). Will talk about these options in more detail in next,next lecture.

## Slide 45: Pipeline Control Path Modifications
All control signals can be determined during Decode
  and held in the state registers between pipeline stages
Read
Address
Instruction
Memory
Add
PC
4
0
1
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
1
0
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
1
0
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
Notes: For lecture

## Slide 46: Example of a Six-Stage Pipelined Processor

## Slide 47: Pipelining & Performance
The Pipeline Depth is the number of stages implemented in the processor, it is an architectural decision, also it is directly related to the technology. In the previous example K=5.
The Stall’s CPI are directly related to the code’s instructions and the density of existing dependences and branches.
Ideally the CPI is ONE.

## Slide 48: Limitations of Pipelines
Scalar upper bound on throughput
  IPC <= 1 or CPI >= 1
Inefficient unified pipeline
  Long latency for each instruction
Rigid pipeline stall policy
  One stalled instruction stalls all newer instructions

## Slide 49: Scalar Unpipelined Processor
One Instruction
resident in Processor
The number of stages
,
K
=
1
Only ONE instruction can be resident at the processor at any given time. The whole processor is considered as ONE stage, k=1.
Scalar upper bound on throughput IPC <= 1 or CPI >= 1
CPI = 1 / IPC

## Slide 50: Pipelined Processor
K –number of pipe stages, instructions are resident at the processor at any given time.
In our example, K=5 stages, number of parallelism (concurrent instruction in the processor) is also equal to 5.
One instruction will be accomplished each clock cycle, CPI = IPC = 1

## Slide 51: Limitations of Scalar Pipelines
Instructions, regardless of type, traverse the same set of pipeline stages.
Only one instruction can be resident in each pipeline stage at any time.
Instructions advance through the pipeline stages in a lockstep fashion.
Upper bound on pipeline throughput.

## Slide 52: Deeper Pipeline, a Solution?
Performance is proportional to (1) Instruction Count, (2) Clock Rate, & (3) IPC –Instructions Per Clock.
Deeper pipeline has fewer logic gate levels in each stage, this leads to a shorter cycle time & higher clock rate.
But deeper pipeline can potentially incur higher penalties for dealing with inter-instruction dependences.

## Slide 53: Stage Quantization
(a) four-stage instruction pipeline
(b) eleven-stage instruction pipeline

## Slide 54: Bounded Pipelines Performance
Scalar pipeline can only initiate at most one instruction every cycle, hence IPC is fundamentally bounded by ONE.
To get more instruction throughput, we must initiate more than one instruction every machine cycle.
Hence, having more than one instruction resident in each pipeline stage is necessary; parallel pipeline.

## Slide 55: Temporal & Spatial Machine Parallelism
A k-stage pipeline can have k instructions concurrently resident in the machine & can potentially achieve a factor of k speedup over nonpipelined machines.
Alternatively, the same speedup can be achieved by employing k copies of the nonpipelined machine to process k instructions in parallel.
K = 1
No Parallelism
Temporal Parallelism
Spatial Parallelism

## Slide 56: Parallel Pipelines
Spatial parallelism requires replication of the entire processing unit hence needs more hardware than temporal parallelism.
Parallel pipelines employs both temporal & spatial machine parallelism, that would produce higher instruction processing throughput.

## Slide 57: Parallel Pipelines
For parallel pipelines, the speedup is primarily determined by the width of the parallel pipeline.
A parallel pipeline with width s can concurrently process up to s instructions in each of its pipeline stages; and produce a potential speedup of s.

## Slide 58: Inefficient Unification into a Single Pipeline
But in execution stages ALU & MEM there is substantial diversity.
Instructions that require long & possibly variable latencies (F.P. Multiply & Divide) are difficult to unify with simple instructions that require only a single cycle latency.

## Slide 59: Diversified Pipelines
Specialized execution units customized for specific instruction types will contribute to the need for greater diversity in the execution stages.
For parallel pipelines, there is a strong motivation to implement multiple different execution units –subpipelines, in the execution portion of parallel pipeline. We call such pipelines diversified pipelines.

## Slide 60: Diversified Pipelines
In a unified pipeline, though each instruction type only requires a subset of the execution stages, it must traverse all the execution stages –even if idling.
The execution latency for all instruction types is equal to the total number of execution stages; resulting in unnecessary stalling of trailing instructions.

## Slide 61: Inefficient Unification into a Single Pipeline
Different instruction types require different sets of computations.
In IF, ID there is significant uniformity of different instruction types.

## Slide 62: Diversified Pipelines
Instead of implementing s identical pipes in an s-wide parallel pipeline, diversified execution pipes can be implemented using multiple Functional Units.

## Slide 63: Advantages of Diversified Pipelines
Efficient hardware design due to customized pipes for particular instruction type.
Each instruction type incurs only the necessary latency & make use of all the stages.
Possible distributed & independent control of each execution pipe if all inter-instruction dependences are resolved prior to dispatching.

## Slide 64: Diversified Pipelines Design
The number of functional units should match the available I.L.P. of the program. The mix of F.U.s should match the dynamic mix of instruction types of the program.
Most 1st generation superscalars simply integrated a second execution pipe for processing F.P. instructions with the existing scalar pipeline.

## Slide 65: Diversified Pipelines Design (2)
In 4-issue machines, 4 F.U.s are implemented for executing integer, F.P., Load/Store, & branch instructions.
Later, designs incorporated multiple integer units, some dedicated for long latency integer operations: multiply & divide, and operations for image, graphics, signal processing applications.

## Slide 66: The Sequel of the i486: Pentium Microprocessor
Mmachine implementing a parallel pipeline of width s=2.
Essentially implements two i486 pipelines, a 5-stage scalar pipeline.

## Slide 67: Pentium Microprocessor
Multiple instructions can be fetched & decoded by the first 2 stages of the parallel pipeline in every machine cycle.
In each cycle, potentially two instructions can be issued into the two execution pipelines.
The goal is to achieve a peak execution rate of two instructions per machine cycle.
The execute stage can perform an ALU operation or access the D-cache hence additional ports to the RF must be provided to support 2 ALU operations.

## Slide 68: Rigid Pipeline Stall Policy
Bypassing
of Stalled
Instruction
Stalled
Instruction
Backward
Propagation
of Stalling
Not Allowed
Notes: Think McDonalds: even though looking over the menu is pipelined with ordering, food prep, and delivery, the two are stalled: if the person in front of you has a special order (no ketchup or pickles) and the employee can’t find it under the heatlamp, all customers behind this customer are stalled. Another model is much better, where ordering is in-order, but food prep and order delivery occur out of order.

## Slide 69: Performance Lost Due to Rigid Pipelines
Instructions advance through the pipeline stages in a lockstep fashion; in-order & synchronously.
If a dependent instruction is stalled in pipeline stage i, then all earlier stages, regardless of their dependency or NOT, are also stalled.

## Slide 70: Rigid Pipeline Penalty
Only after the inter-instruction dependence is satisfied, that all i stalled instructions can again advance synchronously down the pipeline.
If an independent instruction is allowed to bypass the stalled instruction & continue down the pipeline stages, an idling cycle of the pipeline can be eliminated.

## Slide 71: Out-Of-Order Execution
It is the act of allowing the bypassing of a stalled leading instruction by trailing instructions. Parallel pipelines that support out-of-order execution are called dynamic pipelines.

## Slide 72: Characteristics of Superscalar Machines
Simultaneously advance multiple instructions through the pipeline stages.
Multiple functional units => higher instruction execution throughput.
Able to execute instructions in an order different from that specified by the original program.
Out of program order execution allows more parallel processing of instructions.

## Slide 73: Superscalar machine of Degree n=3
The superscalar degree is determined by the issue parallelism n, the maximum number of instructions that can be issued in every machine cycle.
Parallelism = K x n.
For this figure, //’ism = K x n = 4 x 3 =12

## Slide 74: From Scalar to Superscalar Pipelines
Superscalar pipelines are parallel pipelines: able to initiate the processing of multiple instructions in every machine cycle.
Superscalar are diversified; they employ multiple & heterogeneous functional units in their execution stages.
They are implemented as dynamic pipelines in order to achieve the best possible performance without requiring reordering of instructions by the compiler.

## Slide 75: Dynamic Pipelines
Superscalar pipelines differ from (rigid) scalar pipelines in one key aspect; the use of complex multi-entry buffers.
In order to minimize unnecessary staling of instructions in a parallel pipeline, trailing instructions must be allowed to bypass a stalled leading instruction.
Such bypassing can change the order of execution of instructions from the original sequential order of the static code.

## Slide 76: Dynamic Pipelines (2)
With out-of-order execution of instructions, they are executed as soon as their operands are available; this would approach the data-flow limit of execution.

## Slide 77: Dynamic Pipelines (3)
A dynamic pipeline achieves out-of-order execution via the use of complex multi-entry buffers that allow instructions to enter & leave the buffers in different orders.

## Slide 78: Superscalar Execution

## Slide 79: Superscalar Pipeline Stages
In
Program
Order
In
Program
Order
Out
of
Order

## Slide 80: Limitations of Scalar Pipelines
Scalar upper bound on throughput
  IPC <= 1 or CPI >= 1
  Solution: wide (superscalar) pipeline
Inefficient unified pipeline
  Long latency for each instruction
  Solution: diversified, specialized pipelines
Rigid pipeline stall policy
  One stalled instruction stalls all newer instructions
  Solution: Out-of-order execution, distributed execution pipelines

## Slide 82: Extra Slides

## Slide 83: Pentium 4
80486 - CISC
Pentium – some superscalar components
  Two separate integer execution units
Pentium Pro – Full blown superscalar
Subsequent models refine & enhance superscalar design

## Slide 84: Pentium 4 Block Diagram

## Slide 85: Pentium 4 Operation
Fetch instructions form memory in order of static program
Translate instruction into one or more fixed length RISC instructions (micro-operations)
Execute micro-ops on superscalar pipeline
  micro-ops may be executed out of order
Commit results of micro-ops to register set in original program flow order
Outer CISC shell with inner RISC core
Inner RISC core pipeline at least 20 stages
  Some micro-ops require multiple execution stages
    Longer pipeline
  c.f. five stage pipeline on x86 up to Pentium

## Slide 86: Pentium 4 Pipeline

## Slide 87: Pentium 4 Pipeline Operation (1)

## Slide 88: Pentium 4 Pipeline Operation (2)

## Slide 89: Pentium 4 Pipeline Operation (3)

## Slide 90: Pentium 4 Pipeline Operation (4)

## Slide 91: Pentium 4 Pipeline Operation (5)

## Slide 92: Pentium 4 Pipeline Operation (6)

## Slide 93: Introduction to PowerPC 620
The first 64-bit superscalar processor to employ:
  Aggressive branch prediction,
  Real out-of-order execution,
  Six pipelined execution units,
  Dynamic renaming for all register files,
  Distributed multientry reservation stations,
  A completion buffer to ensure program correctness.
Most of these features had not been previously implemented in a single-chip microprocessor.